PEBS:
Positron
Electron
Balloon
Spectrometer
Henning Gast
I. Physikalisches Institut B
RWTH Aachen
DPG07 – 6 March 2007

---
Introduction
Goal: Measure the cosmic-ray positron fraction with a balloon-borne spectrometer.
Motivation: Indirect search for dark matter.
Requirements:
- Large geometrical acceptance:
>1000 cm2sr for 20-day campaign
- Excellent proton suppression of O(106)
- Good charge separation
- Payload weight < 2t
- Power consumption < 1000W
e.g. at 40 GeV: 10-4GeV-1m-2sr-1s-1 x (20x24x3600)s x 0.25m2sr =
43 e+/GeV

---
Prospective performance of PEBS detector
acceptance @100GeV and mission duration
PEBS	2500 cm2sr
20 days
AMS02	500 cm2sr
 1000 days
PAMELA 20 cm2sr
  1000 days
20 days PEBS=
100 days AMS02
7 years PAMELA
94/95/00

---
PEBS design overview
Tracker:
Scintillating fibres (d=250 m) with Silicon Photo-Multiplier (SiPM) readout; power: 260W
Magnet:
Pair of superconducting Helmholtz coils, Helium cryostat,
mean B = 1T, weight: 850kg
Magnet acceptance (width=0.8m, length=0.8m): 4000 cm2sr
Positron acceptance (tracker+ECAL; width=0.76m, length=1m): 2500 cm2sr

---
PEBS design overview
Transition Radiation Detector (TRD):
2 x 8 x ( 2cm fleece radiator + 6mm straw tube Xe/CO2 80:20 )
Electromagnetic calorimeter:
80 x ( 1mm Pb + 8x1 mm2 scintillating fibre + SiPM ) = 14.3 X0, weight: 550kg
Time-of-Flight system (TOF):
2 x 2 x 5 mm3 scintillator, SiPM readout; trigger system!

---
Balloons
OLIMPO experiment (2008)
test balloon launch
altitude profile
NASA ULDB
High-altitude (~40km), long-duration (~20 days) balloon flights from Svalbard balloonport (ASI)
Interesting alternative to space, allows recalibration of experiment as well as multiple journeys

---
Tracker layout
0.80 m
tracker superlayer
2x4x128 fibres
3.2 cm
4 superlayers of 2 layers of double-layered modules of scintillating fibres, d=250 m
stack of fibres accumulates light on SiPM
readout of SiPMs by dedicated VA chip
tracker module
16x1 silicon photomultiplier, strip width 380 µm
need 32x1, 250µm strip width
material budget: 12% X0	( 6% X0 tracker + 6%X0 TRD )
CF skin + Rohacell foam

---
PEBS fibre tracker testbeam setup
AMS02 panel
copper block
cooling pipe
2 fibre bunches:
3x10 square fibres, d=300 m
3 fibres each to SiPM in copper block
beam telescope:
4 CMS Si strip modules
~20m resolution
scintillating fibre bunch + SiPMs
+ PMT
trigger scintillators
trigger scintillators

---
SiPM: example of a MIP spectrum
dark spectrum: beam telescope hit away from fibre
SiPM type 0606EXP
with reflective foil on one side
excess noise:
fibre area =
0.27 x SiPM area
mean: 6.0 photo electrons
4
5
6
3
7
2
8
1
9
0
10
11
12 photo electrons
1 mm
Photonique
SSPM 0606 EXP
S/N=20, eff(0.5pe)=96%
SSPM 050701GR
S/N=100,
eff(0.5pe)=91%

---
Fibre coordinates in beam telescope
%sigma_p over p = sqrt{ a^2 + (b cdot p)^2}
Testbeam results ® PEBS MC simulation ® muon momentum resolution: a=2%, b=0.19%/GeV

---
ECAL shower
tmax
76 cm
16 cm
50 GeV e+
cutout view of ECAL in Geant4 simulation
38 GeV e+
26 GeV e+
14GeV e+
50 GeV protons
dE over dt = E_0 {b^{%alpha +1}} over {%GAMMA(%alpha + 1)} t^%alpha func e^{-bt}
t=x/X0
longitudinal shower profiles
ECAL shower in Geant4 simulation
5 GeV positron

---
ECAL proton rejection and energy resolution
Simulated 40000 positrons and 1700000 protons
proton rejection ~5000 at high energies
ECAL energy resolution

---
TRD design
2 x 8 layers of fleece radiator,
TR x-ray photons absorbed by Xe/CO2 mixture (80:20), in 6mm straw tubes with 30 m tungsten wire
Design equivalent to AMS02 space experiment
radiator
straw tubes
TRD superlayer in G4 simulation
Tasks: proton suppression and
tracking in non-bending plane
2.2 m
10.1 cm
single TRD module
AMS02 TRD octagon integrated at RWTH Aachen workshop

---
TRD performance: positron/proton separation
Analysis of TRD prototype testbeam data
protons
electrons
proton rejection for positron measurement from first 16 layers
TRD 20-layer prototype testbeam data
combined TRD+ECAL rejection of 106 → ~1% proton contamination
proton rejection ~1000

---
Background contributions
40 km altitude: 3.7 g/cm2 remaining atmosphere
primary positrons
atmospheric positrons
misidentified protons
misreconstructed electrons
contributions in absolute numbers for 20-day flight
for efficiency = 50%
composition of positron component according to PLANETOCOSMICS simulation of atmospheric background and contributions from p/e- misidentification

---
Conclusion
Design study to build a balloon-borne spectrometer to measure the cosmic-ray positron fraction, in the context of indirect search for dark matter
Scintillating fibres with SiPM readout as key components, proof of principle established in testbeam at CERN in October 2006
Proton rejection of O(1,000,000) can be achieved with ECAL and TRD
Design study with large acceptance to increase existing data by two orders of magnitude
Expected amount of data from running experiments can be exceeded by an order of magnitude

---
PEBS detector components
Full Geant4 detector simulation available
magnet cryostat
TOF
TRD 1
tracker
TRD 2
ECAL
2.62 m
length: 3.23 m
2.43 m

---
Magnet design
1.90 m
Magnet design by Scientific Magnetics for superconducting pair of Helmholtz coils in He cryostat,
mean field 1 Tesla, opening 80x80x80 cm3,
weight: 850kg
ISOMAX magnet (1998) flown on high-altitude balloon

---
Tracker readout scheme
light collection in scintillating fibre in Geant4 simulation
A
fibre module front view, with SiPM arrays on alternating sides
x
4x1 readout scheme (column-wise) with weighted cluster mean
better spatial resolution than pitch/√12 , depending on p.e. yield
16x1 silicon photomultiplier, strip width 380 µm
need 32x1, 250µm strip width
total power consumption (~50000 channels) of tracker: 260 W

---
PEBS testbeam MC
1 mm
copper block
2 fibre bunches:
3x10 square fibres, d=300 m
3 fibres each to SiPM in copper block

---
Spatial resolution vs angle of incidence
mean=11.2°
35°
distribution of incident angle projected to bending-plane for PEBS detector
p.e. yield of testbeam fibre stack with reflective foil

---
Tracker performance: Momentum resolution
Muon momentum resolution from G4 simulation using testbeam parameters, d = 250µm, B=1T
%sigma_p over p = sqrt{ a^2 + (b cdot p)^2}
p.e. efficiency = 1 x testbeam efficiency
p.e. efficiency = 1.5 x testbeam efficiency
p.e. efficiency = 2 x testbeam efficiency
a = 2%
b = 0.19%/GeV
a = 2%
b = 0.14%/GeV
a = 2%
b = 0.12%/GeV

---
Tracker performance: Angular resolution
median of angular resolution
 = 1 mrad at higher energies
bending plane (fibres): 0.2 mrad
non-bending plane (TRD): 1 mrad

---
ECAL layout
3x3mm2 SiPM
3 mm
8 superlayers of ten layers of lead-scintillating fibre sandwich, with alternating orientation
1mm lead
fibre: 1mm height, 8mm width, read out by SiPMs
14.3 X0 in total, ECAL weight: 550 kg
3x3 mm array: 8100 pixel
76 cm
16 cm
cutout view of ECAL in Geant4 simulation

---
ECAL performance
ECAL energy matching
ECAL shower maximum
positrons
protons
reconstructed momentum
angle between reconstructed track and shower
positrons
protons
positrons
protons
ratio of ECAL energy within one Moliere radius

---
Example event
44.5 GeV positron in event display

---
Intrinsic limits on rejection
example event:
p → p 0 X in very first ECAL layers, momentum reconstruction off by 1.3
0 →  → e.m. shower
intrinsic resolution limited by high-energy 0 production in front of or in first layers of ECAL

---
Intrinsic limits on rejection (2nd example)
example event:
p →p 0 X before last tracker layer
generated: pgen=35.4 GeV
0 momentum: 18.9 GeV →  → e.m. shower
reconstructed: preco=19.5 GeV
intrinsic resolution limited by high-energy 0 production in front of or in first layers of ECAL

---
TRD performance: boron / carbon
compilation of B/C measurements and GALPROP prediction
12C
11B
boron/carbon separation at 5 GeV/n in Geant4 simulation
needs to be studied in more detail

---
TRD performance: antiproton/electron separation
Analysis of TRD prototype testbeam data
electron rejection for antiproton measurement
ECAL +TRD
TOF+TRD