PEBS:
Positron
Electron
Balloon
Spectrometer
Henning Gast
I. Physikalisches Institut B
RWTH Aachen
IDM2008 Conference – Stockholm

---
Introduction
Goal:
Measure the cosmic-ray positron fraction with a
balloon-borne spectrometer.
Motivation:
Indirect search for
dark matter.
Requirements:
- Large acceptance:
    > 0.1m2sr for 20-day campaign
- Excellent proton suppression:
1 in 1 million
- Good charge separation
- Payload weight < 2t
- Power consumption <1000W
protons
positrons

---
Prospective performance of PEBS detector
mSUGRA model (ISAJET+DarkSUSY):
m0=1560 GeV	tan  = 40
m1/2=260 GeV	sgn  = +1
mtop=172.76 GeV	BF=152
neutralino mass: 91.3 GeV
acceptance @100GeV and mission duration
PEBS	0.4 m2sr
100 days
PAMELA 0.002 m2sr
  1000 days
AMS02	0.08 m2sr
 1000 days
aim for first flight in 2012
accumulate statistics in additional flights
100 days PEBS=
52 years PAMELA	1.3 years AMS02
40 days PEBS

---
PEBS design overview
Time-of-Flight system (TOF):
2 x 2 x 5 mm scintillator, SiPM readout; trigger system!
Tracker:
Scintillating fibres (d=250 m),
with Silicon Photo-Multiplier (SiPM) readout; power: 260W
2.2 m
Solar panels:
power for
subdetectors,
communications,
data handling
~600 W
Magnet:
Pair of superconducting Helmholtz coils,
Helium cryostat,
mean B = 0.8T, weight: 850kg

---
PEBS design overview
Transition Radiation Detector (TRD):
2 x 8 x
( 2cm fleece radiator + 6mm straw tube Xe/CO2 80:20 )
Positron acceptance:
0.4 m2sr
2.2 m
Electromagnetic calorimeter:
20 x ( 2mm W + 7.75 x 2 mm2 scintillating fibre + SiPM ) = 11.4 X0, weight: 600kg

---
Balloons
OLIMPO experiment (2009)
test balloon launch
altitude profile
NASA ULDB
High-altitude (~40km), long-duration (~20 days) balloon flights from Svalbard balloonport (ASI)
Interesting alternative to space, allows recalibration of experiment as well as multiple journeys

---
Tracker modules
Hamamatsu MPPC array
3.2 cm
8 superlayers of 25 double-layered modules of scintillating fibres, d=250 m,
stack of fibres accumulates light on SiPM
readout of SiPMs by dedicated chip (VA or SPIROC)
32x1 silicon photomultiplier
250µm strip width, 80 pixels/SiPM
more on the SiPM-fibre-tracker:
NIM A 581 (2007) 423-426
material budget: 12% X0
( 6% X0 tracker + 6% X0 TRD )

---
PEBS fibre module testbeam setup at CERN 06/2008
trigger scintillator
beam telescope:
2 AMS02-
Si strip modules
~20m resolution
fibre module
fibre module
fibre module
fibre module
trigger scintillator

---
Photo electron yield of tracker module
mean photo electron yield:
about 10 photo electrons
idealized SiPM spectrum from Geant4
Hamamatsu SiPM spectrum from testbeam measurements
10 p.e. per cluster ® PEBS MC simulation ® positron momentum resolution: a=3%, b=0.18%/GeV ® MDR=550 GV
%sigma_p over p = sqrt{ a^2 + (b cdot p)^2}

---
ECAL proton rejection and energy resolution
ECAL energy resolution 7% at 100 GeV
determined by
leakage effect and
SiPM dynamic range
Geant4 study
proton rejection ~1000 at high energies
(electron efficiency ~70%)
20 layers in total:
2 mm tungsten +
2 mm scintillator bar +WLS fiber +
2 SiPMs
11.4 X0 in total
ECAL shower in Geant4 simulation
7.75 mm
sandwich calorimeter for 3D-shower reconstruction
5 GeV positron
840 mm

---
TRD design
2 x 8 layers of fleece radiator,
TR x-ray photons absorbed by Xe/CO2 mixture (80:20), in 6mm straw tubes with 30 m tungsten wire
Design equivalent to AMS02 space experiment
radiator
straw tubes
TRD superlayer in G4 simulation
Tasks:
proton suppression and
tracking in non-bending plane
2.2 m
10.1 cm
single TRD module
AMS02 TRD octagon integrated at RWTH Aachen workshop
TRD reference:
NIM A 558 (2006) 526-535

---
TRD performance: positron/proton separation
Analysis of TRD prototype testbeam data
protons
electrons
proton rejection for positron measurement from first 16 layers
TRD 20-layer prototype testbeam data
combined TRD+ECAL rejection of 106 → ~1% proton contamination
proton rejection ~1000

---
Projected performance: mSUGRA example
mSUGRA scan: vary m0, m1/2, tan b, mtop :
check constraining power of current data, identify benchmark points
Ingredients
(using ISAJET+DarkSUSY+Galprop):
top quark mass
relic density of dark matter
anomalous magnetic moment of the muon
b→sγ branching ratio
CR positron fraction
using free boost factor
+ direct search and mass limits

---
Positron fraction c2
PEBS:
vastly improved statistics and
extended energy range
current data
projected PEBS
(without taking detector effects into account)
example benchmark point:
m0= 1560 GeV, m1/2= 260 GeV
tan b = 40, mtop = 172.76 GeV, sgn m = +1, A0 = 0

---
Conclusion
Design study to build a balloon-borne spectrometer to measure the cosmic-ray positron fraction, in the context of indirect search for dark matter
Scintillating fibres with SiPM readout as key components, proof of principle established in testbeams at CERN in 2006-08
Proton rejection of O(1,000,000) could be achieved with ECAL and TRD
Study of physics program ongoing (antiprotons, B/C, ...)
Anomaly in the positron spectrum?
PEBS could answer the question!

---
Acknowledgments
RWTH Aachen
R. Greim, W. Karpinski, T. Kirn, G. Roper, S. Schael, M. Wlochal
EPFL Lausanne
T. Nakada
ITEP Moscow
V. Balagura, M. Danilov
University & INFN Perugia, FBK-irst
G. Ambrosi, P. Azzarello, R. Battiston, C. Piemonte