## Slide 1: AMS-02 TRD
Thomas Kirn
RWTH Aachen University CERN, November 28th

## Slide 2
GeV TeV PeV EeV ZeV
CREAM
TRACER
ATIC
Auger
JEM-EUSO
CROS
Cosmic Ray Fluxes
HEAT
BESS
PAMELA
AMS
E-2.7
E-3.0
E-2.7
Cosmic Ray Composition:
Protons 88 %
Helium 10 %
e- 1 %
e+ 0.1 %
Antiprotons 0.01 %

## Slide 3
TRD
TOF
Tracker
TOF
RICH
ECAL
1
2
7-8
3-4
9
5-6
5m x 4m x 3m
7.5 tons
Upper Tracker
Silicon layer
Inner Tracker
7 Silicon layers
Lower Tracker
1Silicon layer
TRD
Upper TOF 1, 2
TOF 3, 4
RICH
ECAL
Permanent
Magnet
Radiators
AMS-02 – A TeV Particle Spectrometer
ISS Lifetime extended
until at least 2020 / 2028
(March 2010)
→ Switch to AMS-01
permanent magnet
(B=0.14T)
→Tracker reconfigured
→ 'external' layers

## Slide 4
AMS-02 – A TeV Particle Spectrometer
TRD
TOF
Tracker
TOF
RICH
ECAL
1
2
7-8
3-4
9
5-6
TRD
Separation e±:p
Silicon Tracker
Z, P
ECAL
E of e±, γ
RICH
Z, E
Magnet
± Z
TOF
Z, E
Particles and nuclei are defined by their charge (Z) and energy (E ~ P)
Z, P are measured independently by the Tracker, RICH, TOF and ECAL

## Slide 5
AMS-02 – Transition Radiation Detector (TRD)
Choosen configuration for 60 cm height:
20 Layers each existing of:
  22 mm fibre fleece
  Ø 6 mm straw tubes (Xe/CO2 80%/20%)
Non-bending plane: 2x4 layers
Bending plane: 12 layers
p+ rejection >102 1-300 GeV 0.5m2sr

## Slide 6
AMS-02 - TRD

## Slide 7
AMS-02 – Transition Radiation Detector (TRD)
Straw Modules in layer 1 and 2
Straw Modules in layer 20

## Slide 8
AMS-02 – Transition Radiation Detector (TRD)
Layer 20 with radiator on top

## Slide 9
AMS-02 TRD
4 Straw Modules → 1 Readout Group
328 Modules → 82 Readout Groups

## Slide 10
AMS-02 TRD
8 Straw Modules → 1 Gas Tower
41 Gas Towers → 10 Gas Circuits
41 Gas Towers

## Slide 11
AMS-02 TRD: Gas System

## Slide 12
AMS-02 TRD
8 Straw Modules → 1 Gas Tower → 41 Gas Towers

## Slide 13
AMS-02 TRD
41 Gas Towers → 10 Gas Circuits
MF 2
MF 1

## Slide 14
AMS-02 TRD
41 Gas Towers → 10 Gas Circuits
MF 3
MF 4

## Slide 15
AMS-02 TRD Gassystem

## Slide 16
AMS-02 TRD Gassystem

## Slide 17
AMS-02 TRD Gassystem
48 kg
5 kg

## Slide 18
AMS-02 TRD: Radiator

## Slide 19
AMS-02 TRD: Radiator
Radiator LRP 375 BK:
Polyethylene/Polypropylene fibers
Effective fiber diameter: 10 μm
Radiator thickness: 22 mm
Density: 0.06 g/cm3
Cleaning with Dichlormethane CH2Cl2
→ dM/dt ≈ 10-12 g/s/cm2
Inst. f. Organic Chemistry Dichlormethan (CH2Cl2)
4000 individual pieces cut to length

## Slide 20
AMS-02 TRD: Radiator

## Slide 21
AMS-02 TRD: Straw Modules

## Slide 22
AMS-02 – TRD:
Straw Modules
Straw tube proportional counter modules:
Straw tubes: 72 μm multilayer aluminium kapton foil,
Ø 6 mm , 0.8 ÷ 2.0 m length
Wire: tungsten anode wire, 30 μm Ø, tension ≈ 100 g
Gas mixture: Xe / CO2 (80% / 20%) → to be optimized
Operating HV ~ 1460 V → Gasgain of ~ 3000
1 Module → 16 Straws, 100 μm mechanical accuracy
328 Modules → 5248 Straws

## Slide 23
AMS-02 TRD:Gastightness

## Slide 24
AMS-02 TRD: Straw Module Gastightness
→ 8·3y = 24y @ ISS
CO2 Leaktest in Vacuum Straws @ 1bar 1mCH = 16 straws of 1m [+2 endpcs] Typ. Module [1.5m] : 3.1 · 10-5 l mbar/s/mCH ≡ SF 8.2
Gas Tightness measured in safety factors SF, SF=1 → 25.3∙10-5 l mbar/s/mCH

## Slide 25
AMS-02 TRD: Straw Modules;
Wire displacement detection by
Fe55 – Gasgain-Measurement
for controlled shimming
Shim
Fe55
Measurement gauge
Shim

## Slide 26
AMS-02 TRD: Straw Modules,
Wire displacement detection,
Computer Tomography X-Ray
Dicom Image File

## Slide 27
AMS-02 TRD: Straw Modules,
Wire displacement detection by Computer Tomography X-Ray
Controlled Shimming of +200mm y-direction in middle of module

## Slide 28
AMS-02 TRD: Fe55 – Gasgain-Measurements of 328 Flight Straw Modules

## Slide 29
AMS-02 – TRD Straw Modules
Start TRD Integration
September 2004
End TRD Module Integration
October 2005
Module Production on Granite Table
Module Integration in Flight Octagon

## Slide 30
AMS-02 TRD: Straw Modules: Space Qualification Tests

## Slide 31
AMS-02 TRD: Space Qualification Tests
No significant changes in:
Gasgain
Gastightness
→ Straw Modules space qualified

## Slide 32
AMS-02 TRD: Straw Module Longterm Tests
1 Gasgroup → 8 Modules
Fe55 – Monitoring
Pressure-Drop Measurements
Mass-Spectrometer Measurements
Stable Operation for 2 years

## Slide 33
AMS-02 – TRD: Performance, 20 Layer Prototype
Beamtest @ CERN 2000
PS (T9) & SPS (X7, H6):
Recorded events: 3·106
Particles: e-, μ-, π+ 10 - 100 GeV
Protons 10 - 250 GeV
Beam
4 horiz. layers
Gassystem (p,T controlled)
16 vert. layers

## Slide 34
AMS-02 – TRD: Performance, 20 Layer Prototype
Tube Intercalibration
Gasgain-Density-Corr.
Fe55 Energy Calibration

## Slide 35
dE/dX in thin gas-layers V. Ermilova, NIM A 145 (1977) 555
TR gener. and absorp. M. Cherry, Phys.Rev.Lett. D 10 (1974) 3594 Implement. V. Saveliev (HERA-B) G.M. Garibian, NIM A 125 (1975) 133
AMS-02 – TRD: TRD Spectra with Geant 3+ MC

## Slide 36
AMS-02 – TRD: Performance, 20 Layer Prototype
■ AMS TRD 40 GeV Beam

## Slide 37
AMS-02 TRD: Frontend Electronic
UFE-Boards

## Slide 38
VA-Chip Multiplexed Pulsheight Readout
AMS-02 – TRD: Front End Electronic

## Slide 39
358 VA Chips Tests
Select 202 Chips
101 Production of 4 Types PCB
+
Functional Tests
Integration
Series of
Space Qualification
Tests
TVT  3D Vibration
 Coating  TVT
AMS-02 – TRD: Production of UFE-board (FM)

## Slide 40
1st TVT
Temperature : -40oC … +80oC
Pressure : 110-5 mbar
Functional test without failure
Random Vibration
X,Y and Z-Direction
aRMS = 6.8g, 20-2000 Hz for 120 sec
Functional test without failure
Conformal Coating
2nd TVT
Same as 1st TVT condition
AMS-02 – TRD: Space Qualification Tests of UFE-board (FM)

## Slide 41
Operating Temperature (-20 ~ +50 oC)
: Gain Calibration Points
AMS-02 – TRD: Thermal Profile of TVT Test for FM-UFE-Boards

## Slide 42
Common mode noise corrected
Noise = 1.5 ADC == ENC = 4000 e-
AMS-02 – TRD: UFE-Board Noise Measurement after TVT Test

## Slide 43
AMS-02 – TRD: UFE-Board Gain Calibration @ +50°C

## Slide 44
AMS-02 – TRD: UFE-Board Gain Calibration @ -50°C

## Slide 45
Every channel has to
be calibrated within
operating temperature.
AMS-02 – TRD: UFE-Board Gain versus Temperature

## Slide 46
AMS-02 – TRD: FM-UFE-Board Pedestal & Noise Distribution
Pedestal Distribution :
~ 10% of full range
Noise RMS Spread :
~ 4%

## Slide 47
AMS-02 – TRD: FM-UFE-Board Gain & Nonlinearity Distribution
Gain RMS Spread :
~ 3%
Nonlinearity
~ 2E-04 [ADC/fC]

## Slide 48
AMS-02 – TRD: Integration of FM-UFE-Boards on Octagon Wall 1

## Slide 49
AMS-02 – TRD: Integration of FM-UFE-Boards on Octagon Wall 2

## Slide 50
AMS-02 – TRD: Integration of FM-UFE-Boards on Octagon Wall 3

## Slide 51
AMS-02 – TRD: Integration of FM-UFE-Boards on Octagon Wall 4

## Slide 52
AMS-02 – TRD: Integration of FM-UFE-Boards on Octagon Walls
5
6
7
8

## Slide 53
AMS-02 TRD: Straw Module+Frontend-Readout,
Corona Discharges

## Slide 54
AMS-02 TRD: Corona Discharge Test
Epoxy Potting
Conformal Coating
Straw Module UTE-board
HV plug/receptacle
HV cables
HV-Distribution (UHVD) board

## Slide 55
Octagon-Like Al. Panel
Complete Single HV & Readout Unit
UFE
VA2
VA2
UHVD
To UDR2
AMS-02 TRD: Corona Discharge Test
2nd VA
1st VA
UHVD

## Slide 56
AMS-02 TRD: Corona Discharge Test
HV Plug/Receptacle
UHVD
UFE
TRD 4 layers straw modules
HV Cables

## Slide 57
ArCO2, 1 l/h
AMS-02 TRD: Corona Discharge Test
With Kapton Screening of UTE-boards no Corona discharges observed!

## Slide 58
AMS-02 TRD: ElectroMagnetic Interference Test
Octagon-Like Housing
4 straw modules + UFE-Readout
Multilayer Insulation Screen
EMI Test @KMW Co. Munich
According to
“Space Station Electromagnetic Emission and Susceptibility Requirements for the Electromagnetic Compatibility”
SSP30237 paragraphs RS02, RS03, and RE02
Electric field sensor
EMI emitter
Wave : Horizontal / Vertical Polar. Frequency range : 10 kHz ~ 1 GHz Electric Field : 5 ~ 100 [V/ m]

## Slide 59
AMS-02 TRD: ElectroMagnetic Interference Test
Freq. =10 kHz ~ 200MHz
|E|rms = 5 [V/m] w. V.P.
Noise VP = 1.782 +- 0.0159[ADC]
200MHz ~ 1GHz, 70 [V/m]
Noise VP = 1.808 +- 0.0279[ADC]
Noise HP = 1.781 +- 0.0333[ADC]
14kHz ~ 20MHz, 50~100[V/m]
Noise VP = 1.82 +- 0.0332[ADC]
Sweeping Freq. =14 kHz ~ 30MHz
|E|rms = 20 ~ 100[V/m] w. V.P.
Noise VP = 1.839 +- 0.0554[ADC]
Sweeping Freq. =30MHz ~ 1GHz
|E|rms = 20 ~ 100[V/m] w. V(H).P.
Noise V&H = 1.804 +- 0.0613[ADC]

## Slide 60
AMS-02 TRD: ElectroMagnetic Interference Test
Before shielding
After appropriate shielding of cables
Acceptable Limit Line for Full TRD
Acceptable Limit Line for one UFE

## Slide 61
AMS-02 TRD DAQ

## Slide 62
AMS-02 TRD DAQ
328 Modules → 82 Readout Groups
2 FM U-Crates, 2 FM UPD-Crates

## Slide 63
AMS-02 TRD DAQ

## Slide 64
AMS-02 TRD DAQ
Space requirements issued by NASA :
Electromagnetic Interference
Electromagnetic Compatibility
Mechanical Vibration
Thermal Vacuum Test
TRD Power Consumption
UFE (20W) + UCrate (41W) + UPD (36W)
 100W

## Slide 65
AMS-02 TRD DAQ

## Slide 66
AMS-02 TRD DAQ

## Slide 67
AMS-02 TRD DAQ

## Slide 68
AMS-02 TRD DAQ

## Slide 69
AMS-02 TRD DAQ

## Slide 70
AMS-02 TRD DAQ

## Slide 71
AMS-02 TRD DAQ

## Slide 72
AMS-02 TRD DAQ

## Slide 73
AMS-02 TRD DAQ

## Slide 74
AMS-02 – TRD M-Structure, Heating

## Slide 75
AMS-02 – TRD M-Structure Heating

## Slide 76
AMS-02 – TRD M-Structure, Heating

## Slide 77
AMS-02 – TRD M-Structure Heating

## Slide 78
AMS-02 – TRD M-Structure Heating

## Slide 79
AMS-02 – TRD M-Structure Heating

## Slide 80
AMS-02 – TRD M-Structure Heating

## Slide 81
AMS-02 – TRD M-Structure Heating

## Slide 82
AMS-02 – TRD M-Structure Heating

## Slide 83
AMS-02 – TRD M-Structure Heating

## Slide 84
AMS-02 – TRD M-Structure Heating

## Slide 85
AMS-02 – TRD M-Structure Heating

## Slide 86
AMS-02 – TRD Thermostats Space Qualification

## Slide 87
AMS-02 – TRD Flight Integration, System Test

## Slide 88
AMS-02 – TRD Flight Integration,
Gastightness @ RWTH Aachen Cleanroom
He-dp/dt-Measurements of
individual straw modules
during production:
qWall 7 = 1.56*10-2 l mbar/s
qWall 3= 1.53 * 10-2 l mbar/s
→ Safety Factor 8 for CO2

## Slide 89
AMS-02 – TRD
TRD Delivery to CERN October 2007

## Slide 90
AMS-02 – TRD Flight Integration,
Gastightness @ AMS Cleanroom CERN
Ar/CO2- (80%/20%) dp/dt-Measurements
of whole TRD after delivery to CERN
end of 2007:
qCO2= 0.29 * 10-2 l mbar/s
Comparison Measurement dp/dt in air:
He ↔ CO2 Factor of 2
Factor 5 20% to 100 % CO2
qHe = 3.09*10-2 l mbar/s
→ TRD gastight

## Slide 91
AMS-02 – TRD Flight Integration,
Gastightness @ AMS Cleanroom CERN
Ar/CO2- (80%/20%) dp/dt-Measurements
of whole TRD after pre- & de-integration
End of 2008:
qCO2= 0.29 * 10-2 l mbar/s
Comparison Measurement dp/dt in air:
He ↔ CO2 Factor of 2
Factor 5 20% to 100 % CO2
qHe = 3.09*10-2 l mbar/s
→ TRD gastight

## Slide 92
AMS-02 – TRD
TRD Flight Integration July 2010

## Slide 93
AMS-02 @ CERN Cleanroom

## Slide 94
AMS-02 @ ESTEC, Noordwijk
AMS-02 inThermal Vacuum Chamber
No major issues

## Slide 95
AMS-02 @ ESTEC, Noordwijk
AMS-02 in EMI Chamber
EMI emission profile:
  Range 30 Hz – 50 MHz
  Limit set by Nasa not exceeded
EMI susceptibility (not shown):
  Interference at 80 MHz (TDCs)
  No major issues
Electromagnetic Interference Test:
  Emission
  Susceptibility/Immunity

## Slide 96
AMS-02 – Test Beam H8 CERN
8-20 Aug 2010
e± Energy Resolution: 2.5-3%
Energy

## Slide 97
AMS-02 Transport CERN to KSC
AMS-02 in the Space Station Processing Facility (SSPF), ready for installation into the Space Shuttle
Extended data taking periods to verify detector performance
February 2011
Arrival of US Air Force C5 Galaxy
at Geneva – 25 Aug 2010

## Slide 98
AMS-02 in Endeavour Payload Bay, Closing of Doors

## Slide 99
AMS-02 - STS 134 Launch
16th of May

## Slide 100
AMS-02 - TRD: First Slow Control Data

## Slide 101
AMS-02 - Start Data Taking 09:35 CDT, May 19th 2011

## Slide 103
AMS-02 - Start Data Taking 09:35 CDT, May 19th 2011
AMS-02 - Trigger Rate
More than 15 Billion Triggers recorded

## Slide 104
AMS-02 TRD

## Slide 105
AMS-02 TRD
TRD Hits per event

## Slide 106
AMS-02 TRD - Occupancy

## Slide 107
AMS-02 TRD - Occupancy
AMS TRD Occupancy
5246/5248 Channels within specification.

## Slide 108
AMS-02 TRD – Amplitude/Noise
Noise
Amplitude on track
Pedestal

## Slide 109
AMS-02 TRD – Temperature Monitoring
Min ~11°C
Mean ~15°C
Max ~19°C

## Slide 110
AMS-02 TRD – Temperature Monitoring

## Slide 111
AMS-02 TRD – Temperature Monitoring
TRD inside temperature
ΔT = 1 °C
oC
May 23 to June 1

## Slide 112
AMS-02 TRD – Pressure Monitor
Total leak rate of 4.2 mbar/day:
→ CO2: (1.5 + 0.125*2.7) mbar/d = 1.84 mbar/day
Volume* leak rate = 230 l ∙ 1.84 mbar/day = 422.6 l mbar / day
→ 0.764 g /day = 8.85 μg / s (before launch 6 μg / s )
Total storage: 5kg
→ CO2 lasts for 17.9 years > ISS Lifetime

## Slide 113
AMS-02 TRD Raw Data, before 1st Calibration
AMS TRD Proton Spectrum
Single Straw
HV
1580V
HV -20V

## Slide 114
AMS-02 TRD Raw Data, before 1st Calibration
HV
-100V
HV
1580V
HV -20V

## Slide 115
AMS-02 TRD Raw Data, before 1st Calibration
AMS TRD Proton Spectrum
Single Straw
HV
-100V
HV
1580V
Gas Refill,
HV +50V
HV -20V

## Slide 116
AMS-02 TRD after 1st Calibration

## Slide 117
Helium (Z=+2, 10.0 GeV/c < P < 20 GeV/c)
Day 138 - 220
AMS-02 TRD after 1st Calibration, He-Sample

## Slide 119
Protons
Electrons
Helium
Protons
Electrons
Single Straw Spectrum
frequency
Helium
AMS-02 TRD Response to Protons, Helium, Electrons
Use ToF, Tracker and ECAL to define clean single track proton, helium and electron samples

## Slide 120
AMS-02 TRD Proton Rejection
He ?
6200 @ 90%
80% Efficiency, Proton Rejection = 32541 (33302) Cut at 0.48
90% Efficiency, Proton Rejection = 6208 ( 6328) Cut at 0.53
P = 3 - 50 GeV
Electrons
Protons

## Slide 121
AMS-02 TRD Proton Rejection

## Slide 122
AMS-02 TRD Proton Rejection
TRD
ECAL-BDT
3D-Shower Shape
All
Positrons
Electrons
TRD-LLH & ECAL-BDT

## Slide 123
AMS-02 TRD
Slow Control and Data Monitoring

## Slide 124
TRD/TRDGas-System Monitoring Programs

## Slide 125
TRD/ACC/TAS-Standard Shift

## Slide 126
List of TRD/TRDGas Programs
Electronics Monitoring:
TRD Status Monitor (TRD-S)
Pedes_Canvas
UDR_HK_Canvas
Read_block_files
UHV Status Monitor (UHV-S)
Gas Monitoring:
TRDGAS Monitor (TRDGAS-M)
TRDGAS Status Monitor (TRDGAS-S)
TRD Pressure Monitor (Pressure Monitor)
Detector Monitoring:
TRD Data Monitor (TRD-M)
TRD-DTS Monitor (TRDDTS-M)
TRD-GainMonitor (TRD-GainMonitor)

## Slide 127
TRD-ACC-TAS SHIFTER:
TRDGas Standard Monitoring Shift
Start-up of AMS-Activation:
AMS Power-Step-1 from CMD Post
- Initializes TRDGAS Crate (UG)
- Configures and starts UG CtrlTsk
- Activates UG Q-List items 7A/7B HV ON: CMD asks if TRD Gas is ok
Standard Shift Activity:
• No TRDGAS commanding in standard shift • Adjust TRD HV once per day by a 3V step (MOP-ADC value ≈ 60)
details see pages 131-133
Check: TRDGAS monitor data available All plots in TRDGAS-M update • Check: Pressures and Temperatures in range TRDGAS-S is updating regularly

## Slide 128
TRD-ACC-TAS SHIFTER:
TRDGas Emergency Actions
Emergency Actions from TRD Post CALL EXPERT ASK for Commanding
- Xe/CO2 Vessel High Pressure (>175/100bar) UG Heaters DISABLE
- Xe/CO2 Vessel High Temperature (>+60°C) UG Heaters DISABLE
- Xe/CO2 Vessel Low Temperature (<-20°C) HEAT VESSELS (UG-A)
- Xe/CO2 Vessel Low Temperature (<-40°C) HEAT VESSELS (UG-B)
Requires UGPD-B powered and all DC/DC on
- Xe/CO2 Vessel Low Temperature (<-50°C) Turn AMS into sun
Mixing Vessel High Pressure (>13bar) VENT MIX - Box-C High Pressure (>1500mbar) VENT Box C
TRD High Pressure (>1300mbar) Flipper Valves CLOSE - TRD Low Pressure (< 900mbar) Flipper Valves CLOSE ask CMD: TRD HV OFF
TRD-SidePanel High Temperature (>+40°C) Flipper Valves CLOSE Ask CMD to disable TRD 120V Heaters (PDS 120V Heater #3) - TRD-SidePanel High Temperature (>+50°C) ask CMD: TRD StandBy Option: ask CMD for AMS StandBy last Option: Turn TRD away from sun - TRD-SidePanel Low Temperature (<+5°C) Flipper Valves CLOSE Ask CMD to switch ON TRD 120V Heaters A & B (PDS 120V Heater #3)
- TRD-SidePanel Low Temperature (<-20°C) Turn AMS into sun

## Slide 129
TRD-ACC-TAS SHIFTER:
TRD Standard Monitoring Shift
• Check: TRD data monitor (TRD-M, Pedes_Canvas.ps, UDR_HK_Canvas) • Check: TRD Temperatures in range (TRDGAS-S and TRD Sidepanels)
Emergency Actions from TRD Post CALL EXPERT ASK for Commanding
TRD HV Trip! ASK Command to stop DAQ
  Go to TRD-HV
  reset HV by pressing
  button `HV On´

## Slide 130
TRD-ACC-TAS SHIFT SETUP

## Slide 131
Screen 1 Left (TRD/GAS)

## Slide 132
Screen 1 Right

## Slide 133
Screen 2 Right

## Slide 134
Screen 3 Right!

## Slide 135
Screen 4 Right!

## Slide 136
Screen 5 Right!

## Slide 137
TRD Monitoring:
TRD Status Monitor (TRD-S)
  Pedes_Canvas
  UDR_HK_Canvas
Read_block_files
TRD Data Monitor (TRD-M)
TRD-DTS Monitor (TRDDTS-M)
GainMonitor (GainMonitor)

## Slide 138
Configuration of TRD-S
Set X to 2
left-click ↑ number
right-click ↓ number
Set Directory to
Data/BLOCKS/SCIBPB/RT
and
Data/BLOCKS/HKLR/CDP
Find Last File
(left click)
Read continously
(right click)
Load for reading
(left click)
Check:
Every box green,
HV value match the settings,
browser for warnings/errors

## Slide 139
TRD-S
JMDC
QList
BLOCK
Files
Commands
from ground
DAQ and
SC Status
All information from TRD Readout is analyzed and summarized
in overall status for shift taker

## Slide 140
UHV Status Monitor:
Go to RUN directory and open programm:
  cd ~/RUN
  UHV-S &
Set to current directory and file
Use to check single channel HV values for A/B-Side
Screen-3: Additional Tools for TRD Experts
Set Directory to
Data/BLOCKS/HKLR/CDP

## Slide 141
Calibration of each of the 5248 Straw-Tubes
Upper left: Actual Pedestal values in ADC channels
Upper Right: Difference between actual and default Pedestal values
Lower Left: Actual Noise values in ADC channels
Lower Right: Difference between actual and last Pedestal values
Noise should show usual pattern
(all but 2 channels green for A-Side Power,
also slightly higher noises on end/front of segment for B-Side Power)
Pedes_Canvas.ps

## Slide 142
Upper: Actual Occupancy (number of hits in each of the 5248 straws)
Lower: Actual Amplitude (Median, Pedestal corrected) values in ADC channels
for each of the 5248 straws
Occupancy plot should not show any unusual high or low channels
Amplitudes should be fairly homogenous
UDR_HK_Canvas.ps

## Slide 143: TRD-DTS Monitor – TRDDTS-M
A total of 404 Dallas Sensors on 40 strips are read out by USCM-UG-A/B (202 sensors – 20 strips – 7 busses respectively)
The Label contains Layer-Number L01..L20, Tower-Number T-9..T+9 and position along chamber in decimeters [XY]-10..[XY]+10
Some sensors on the strips are located outside of the octagon volume (near the connector patch-panel). For those sensors the naming scheme is as follows: Layer-Number P01..L20, Wall-Number W1..W8 (W1 = +X, W3=+Y, W5=-X, W7=-Y, Wall-Half[+-][XY]

## Slide 144
Time of last
update
On any sensor:
Left click -> get sensor
information
Right click-> get histogram of
sensor temperature
(close histogram
again using the
‘Return’ button!)
Change color range

## Slide 145: Usage: TRD-DTS Monitor– TRDDTS-M
Each button represents the approx. location of 1A & 1B sensor
A left-/right-click on a button shows detailed information/ Temp.history of the sensor
‘Last update’ supposed to stay green in ‘Read’-mode
Color palette adjustable left-/right-click on maxor min button increases/decreases respective limit by 1
On bottom right the active readout side is shown – in case both readouts are available one can select which one shall be displayed
Different views available (click on ‘Name’ button on bottom)

## Slide 146: GainMonitor
Gain Monitor:
The HV of the TRD has to be adjusted every day to minimize the gas
gain variations.
The MOP should be at about 60 ADC counts.
For checking the evolution of the TRD signal gain, open a terminal, go to
RUN directory and open program:
  cd ~/RUN
  TRD-GainMonitor &
Take care that you do not hit any key
afterwards (causes hang-up)
Be patient, especially when you ask
for updating.

## Slide 147: GainMonitor
Type in your
CERN AFS user name
Click on update
You are then prompted in the terminal window:
  Your_user_name@ams.cern.ch password:

## Slide 148: GainMonitor
You can enlarge the
scale by selecting an
interval on each axis
Click on unzoom for returning to complete data set
You can deduce the actual value by
estimating the slope.
(Be careful, data may be several hours old!)

## Slide 149
TRDGas Monitoring
TRDGAS Status Monitor (TRDGAS-S)
UG CHD (Critical Health Data)
TRDGAS Monitor (TRDGAS-M)
Pressure Monitor (Pressure Monitor)

## Slide 150
TRD/TRDGas-System

## Slide 151
TRDGas-System

## Slide 152
TRDGAS Supply Vessel Limits
Supply Vessels: Pressure-Temperature dependency
Vessel: Xenon CO2 MIX
100% Fill Level: 48kg 5kg Max.Op.Press. 175bar 100bar 14bar
Max.Des.Press. 207bar 220bar 20bar
Proof Press. 335Bar 330bar 40bar
Burst Press. 645Bar 440bar 80bar
Min.Des.Temp. -70°C -70°C
Max.Des.Temp. +65°C +65°C
Gas Freezing -110°C -55°C

## Slide 153
TRDGAS Sensor Value Limits
UG-Supply-Current [92] Monitoring: 0.6A
Pump HalfSpeed: +0.1A
Heat Vessels:
Heat for Mix: +1.0A
Marotta Valve: +1.2A
BoxC Canister Relief Valve at Inlet: 1.7bar
TRD Pressure: 900-1300 mbar
Pump HalfSpeed: Psup +320mbar Pret -320mbar
MfdP [96..99]: 0 +- 20 mbar
Temp [89/94]: -20°C .. +55°C
NO BOX-S/C Marotta-Valve Operations below 0 °C
NO Pump Operation below +5°C [94-SP blk]
Temp UGSCM/UGPD [70] -15°C .. +45°C

## Slide 154
Configuration of TRDGAS-S
Set X to 2
left-click ↑ number
right-click ↓ number
Set Directory to
Data/BLOCKS/HKLR/CDP
Find Last File
(left click)
Read continously
(right click)
Load for reading
(left click)
Every box should be green,
Temperature and Pressure values should be in the operating ranges,
check the browser for warnings or errors

## Slide 155
TRDGAS-S
Temperatures:
All TRDGas
DTS-Sensors
Range:
-30°C to +50°C
Pressures TRDGas:
Xe/CO2 / Mix. Vol.
Range:
Xe: <150 bar
CO2 : < 80 bar
Mix.Vol.: < 4.6 bar
SidePanel DTS-Sensors:
Ranges: +5°C to +40°C
Pressures TRD:
BoxC
Range:
Pump off: 900 to 1500 mbar
Pump on half speed:
P3: 1220 to 1820 mbar
P4: 580 to 1180 mbar
(dP(In) – dP(out)) / 2 = 0 ± 50 mbar

## Slide 156
UG CHD (Critical Health Data)
Bit Definition:
UG-CHD Bits from UG-CtrlTask
Monitor MultiCast Server:
$ TRDCHD-M -m MCC (Shuttle)
-m HOSC (ISS)
STA INV – not updated
-> UG-Task running ?
XE P 20.. 175bar
CO2 R 10.. 100bar
MIX E 0.. 13bar
BXC S 800..1200mbar
DRP S Pin-Pout = 0 / 650mbar
For CP off half
LEAK detected by UG-CtrlTask
XE T -30..+60degC
CO2 E -50..+60degC
PH M -15..+60degC
MVS P -15..+60degC
MVC E -15..+60degC
BXC R +5..+40degC
MIX T -15..+60degC

## Slide 157: TRD-Gas Monitor Program: TRDGAS-M
Dir: selected interface File: DDDD/NNN
right-click READ
PDS-UGPD current
from PDS
Other Data from UG
(1st DTSdata after 5min)
JMDC output in terminal

## Slide 158: TRD-Gas Monitor Program: TRDGAS-M

## Slide 159: TRD-Gas Monitor Program: TRDGAS-M

## Slide 160: TRD-Gas Monitor Program: TRDGAS-M

## Slide 161: TRD-Gas Monitor Program: TRDGAS-M

## Slide 162: TRD-Gas Monitor Program: TRDGAS-M

## Slide 163: TRD-Gas Monitor Program: TRDGAS-M

## Slide 164: TRD-Gas Monitor Program: TRDGAS-M

## Slide 165: TRD-Gas Monitor Program: PressureMonitor
Actualize data
Chose Time Range,
Start (Calendar) End
Set chosen
time range
Fit to temperature
corrected pressure
in chosen time range
Save 3 Canvas
As png-file