## Slide 1
TRD Operations
T. Siedenburg
AMS DOE Review Sep-2013

## Slide 2
Transition Radiation Detector (TRD)
Particle Momentum TR
Electron 0.5 GeV – 1 TeV YES Proton 0.5 GeV – 1 TeV NO
e
p
TRD
TOF
Tracker
TOF
RICH
ECAL
1
2
7-8
3-4
9
5-6



















TRD
Transition Radiation (TR)
Rare soft gamma ray emission (5 keV)
when high energy charged particle crosses a material boundary
Nondestructive separation of light from heavy relativistic particles in addition to ECAL e.m. shower e / p: Transition Radiation Ions: Ionisation (dE/dX)

## Slide 3
e
p
Proven design for ground based TRDs μ-fiber fleece radiator Xenon gas TR photon absorber Xe-CO2 proportional counters
Straw tubes (6mm Ø, 1-2m length)
Thin kapton walls (72 μm)
dE/dX
TR
Analogue pulseheight readout
20 layers radiator / modules for sufficient proton rejection
Orientation along X and Y for 3D particle tracking
AMS TRD Design for optimal performance
100 GeV Protons
20 GeV Electrons
AMS TRD Prototype Beamtest Single Tube Spectra
─ Simulation
○□ Data

## Slide 4
AMS TRD: Gas Straw Tube Detector for Space
Optimized for space environment
Selection of best straw tubes -
gastight to diffusion level in vacuum
Stable support to survive launch
Robust Gas Supply System - storage of consumables for > 20 y of operation
- flexible Xenon / CO2 mixing
- segmentation to isolate potential leaks
Active environment stabilization to reduce
sensitivity to thermal environment (MIT, Burger)
Redundant monitor/control/DAQ electronics

## Slide 5
AMS TRD: Space Qualified Construction
Modules with 16 straw tubes
Carbon-fiber stiffeners
End pieces:
Gas In/Out HV / Signal
Octagonal thermally stable
carbon-fiber support structure
for 328 modules in 20 layers.
Fleece radiator interleaved
4+4 layers in bending plane
12 center layers perpendicular
Mechanical accuracy 100 μm to assure wire is centered.
Verified with 3D measurement for all module support points.
TRD system instrumented with:
24 heaters 62 thermostats 82 HV distribution boards
82 AD readout boards 482 temperature sensors 9+20 pressure sensors
60 cm Space Qualification Module
IN
OUT
GAS
SIG
HV
2m

## Slide 6
18 W
Low Power DAQ for 5248 channels
HV Distribution 64 Chan. FrontEnd RWTH Aachen
Common AMS Framework
Koutsenko, Kounine, Capell, Lebedev, Rozhkov (MIT)
HV Supply Data-Reduction 10 kB →150 B/Evt
Power Supply
ReadOut Crates, each with 14 twofold redundant boards
PowerSupply1
PowerSupply0
ReadOut1
ReadOut0

## Slide 7
AMS TRD assembled for flight
1,5 m3 instrumented volume, 5248 channels in 20 layers Provides electron-proton separation and 3D tracking

## Slide 8
TRD Gas System
Supply System
Carbon overwrapped
Pressure vessels
Xenon: 49 kg
CO2: 5 kg Mixing vessel
Solenoid valves
Heaters / Thermostats
Pressure sensors
Temperature sensors
Circulation System
Canister enclosure for
Circulation pumps
Spirometer
Solenoid valves
Heaters / Thermostats
Pressure sensors
Temperature sensors
Distribution System
4 Manifolds with
Solenoid flipper valves Differential pressure sensors
10 Gas groups of 23 l each
CP
Simplified schematics
Gas mixing does not affect TRD data quality

## Slide 9
TRD Gas Supply System assembled for flight

## Slide 10
TRD Two Years of Operation Experience
For European night shift TRD monitoring covered
by ASIA POCC since Aug-2012
TRD Post at CERN POCC

## Slide 11
Primary Shift Objective: Safety
Keep the TRD within safe operation limits
- 24/7 monitoring of pressure and temperature sensors
High pressure supply vessels / mixing vessel / TRD straw tubes
- Prompt action in case of problems
Operate TRD heaters / valves / pumps
- Initiate preventive actions for expected low temperature environment
Dependent on ISS orbit beta, attitude and radiator/solar-array config. in coordination with AMS Thermal group (MIT, Burger)
Operate TRD heaters / valves / pumps
Request ISS solar-array / radiator operations
TRD Two Years of Operation Experience

## Slide 12
18oC
10oC
Verify functionality of TRD Heaters
Thermostat switching points 10/20 oC
Correlate with AMS Thermal (MIT, Burger)
Offline data analysis: temperature(density)
dependent gain correction
Relative Signal S Relative Density D Ionis.: ΔS = -5·ΔD
TRD Two Years of Operation Experience
GMT 2011-06-11 16:42
Temperature Sensors on TRD Modules
TRD top view
S
1.0
TRD Prototype BeamTest
muons
1.00

## Slide 13
AMS Physics Shift Objective: Signal Quality
Keep the TRD signal response at optimal working point
- 24/7 monitoring of 5248 straw tube signals
Verification of signal baseline calibrations and signal homogeneity
Check TRD event size, which regularly increases in the South Atlantic Anomaly
Request AMS-LEAD to re-calibrate or re-initialize in case of problems
- 24/7 monitoring of 82 high voltage channels
Prompt reset of tripped HV channels
Switch off HV in case of severe data rate problems (e.g. high solar activity)
Daily adjustment of HV – coordinated with LEAD
- 24/7 monitoring of TRD gas tightness and gas composition
Prompt isolation of potentially leaky gas sections
Monthly refill of Xenon / CO2 mixture – coordinated with LEAD and Thermal Group
TRD Two Years of Operation Experience

## Slide 14
Daily TRD HV adjustment by TRD expert
Steady increase of TRD signal height due to gas-gain increase from diffusion gas losses
Compensate with HV adjustment adapted to signal response since previous adjust
Complex multi-step procedure that occasionally fails –
Requires prompt recovery depending on reason and step of failure
Stable TRD Signal height since Nov-2011:
Signal height
21
Proposed HV adj. -3V
60
62
58
*
*
20
19
18
17
22-May-2013
From science data analysis
Signal height
60
120
0
May-19-2013
May-19-2011
TRD Two Years of Operation Experience
Procedure involves manual AMS DAQ Stop and Restart with new TRD HV settings
Improved in Oct-2011 to take less than 5 minutes – since then performed daily

## Slide 15
Gas Refill Objectives
TRD Gas losses: 4.5 mbar / day * 230 l (1.0 mbar/d CO2 + 3.5 mbar/d Xenon)
Xenon CO2 Diffusion Leak
8680 l 2630 l initial supply at 10oC
465 l 200 l refills 5/11 – 5/13 monthly refill: 20 l Xe + 6 l CO2
34 y 34 y lifetime with standard refills standard since June 2012
Operate TRD at optimal conservative working point Keep sufficient margins for gas supply resources
TRD Two Years of Operation Experience
TRD Pressure
1200
CO2 Fraction
May-19-2011 Date May-19-2013
20%
10%
Stable 90/10 Xe/CO2 Operation since June 2012
mbar
800
1000
small gas leak observed identified & quantified

## Slide 16
Summary
Stable TRD operation since launch with no major failure
Daily HV adjustment to keep TRD signal constant since Nov-2011
Monthly TRD gas refill for stable 90/10 Xenon/CO2 since Jun-2012
Adaptation of refill command sequences – valve opening times and actuations
To keep TRD fully operational at optimal performance requires
careful monitoring and adjustments from shift personel and experts
TRD Two Years of Operation Experience